## Slide 1: Hardware
Computing Components

## Slide 2: Chapter Goals
  Read an ad for a computer and understand the jargon
  List the components and their function in a von Neumann machine
  Describe the fetch-decode-execute cycle of the von Neumann machine
  Describe how computer memory is organized and accessed
Name and describe different auxiliary storage devices
Explain the concept of embedded systems and give examples from your own home

## Slide 3: Computer Components
Consider the following ad:
Be patient! If you
don’t know now,
you should know
shortly

## Slide 4: Sizes in Perspective
Admiral Grace Murray Hopper’s Illustration
  A coil of wire nearly 1,000 feet long
      Distance traveled by an electron along the wire in the space of a microsecond
  A short piece of wire
      In the space of a nanosecond
  A bag containing grains of pepper
      In the space of a picosecond

## Slide 5: Sizes in Perspective
What is a Hertz?
Powers of 10 for time, powers of 2 for storage

## Slide 6: Sizes in Perspective
Intel Processor
speed 2.66 GHz
SDRAM
size 4GB
speed 800 MHz
500GB SATA at 5400 RPM
Transfer rate 300MB per second
Flat screen dot pitch .28mm
To which do these
apply?
Bigger is better
Faster is better
Smaller is better

## Slide 7: Stored-Program Concept
Instructions and data both stored in memory unit

## Slide 8: Input/Output Units
Input Unit
A device through which data and programs from
the outside world enter the computer system;
Can you name three?
Output unit
A device through which results stored in the
computer memory are made available outside the computer system
Can you name two?

## Slide 9: Touch Screens
Touch screen
A computer monitor that can respond to the user, touching the screen with a stylus or finger
There are four types
  Resistive
  Capacitive
  Infrared
  Surface acoustic wave (SAW)

## Slide 10: Touch Screens
Resistive touch screen
A screen made up of two layers of electrically conductive material
  One layer has vertical lines, the other has horizontal lines
  When the top layer is pressed, it comes in contact with the second layer which allows electrical current to flow
  The specific vertical and horizontal lines that make contact dictate the location on the screen that was touched

## Slide 11: Touch Screens
Capacitive touch screen
A screen made up of a laminate applied over a glass screen
  Laminate conducts electricity in all directions; a very small current is applied equally on the four corners
  When the screen is touched, current flows to the finger or stylus
  The location of the touch on the screen is determined by comparing how strong the flow of electricity is from each corner

## Slide 12: Touch Screens
Infrared touch screen
A screen with crisscrossing horizontal and vertical beams of infrared light
  Sensors on opposite sides of the screen detect the beams
  When the user breaks the beams by touching the screen, the location of the break can be determined

## Slide 13: Touch Screens
Surface acoustic wave (SAW)
A screen with crisscrossing high frequency sound waves across the horizontal and vertical axes
  When a finger touches the surface, corresponding sensors detect the interruption and determine location of the touch

## Slide 14: Memory
Memory
A collection of cells, each with a unique physical address
Most computers are byte-addressable
Cell at address 11111110 contains 10101010

## Slide 15: Memory
Memory
What does 10101010 mean?
No way to answer that
Could be an instruction, a natural number, a signed integer, a character, part of an image, …

## Slide 16: Memory (Primary), cont’d
Uses random access:
2 basic operations:
  Fetch (addres)
  Store (address, value)

## Slide 17: RAM and ROM
Random Access Memory (RAM)
Memory in which each location can be accessed and changed
Read Only Memory (ROM)
Memory in which each location can be accessed but not changed
RAM is volatile, ROM is not
What does volatile mean?

## Slide 18: Secondary Storage Devices
Why is it necessary to have secondary storage devices?
Can you name some of these devices?

## Slide 19: Magnetic Tape
The first truly mass auxiliary storage device was the magnetic tape drive
Tape drives have a
major problem; can
you describe it?

## Slide 20: Magnetic Disks

## Slide 21: Magnetic Disks
Seek time
Time for read/write head to be over right track
Latency
Time for sector to be in position
Access time
Can you define it?
Transfer rate
Rate at which data moves from the disk to memory

## Slide 22: Magnetic Disks
3.5 floppy – epson SMD 1340 Specifications:
# sectors per track: 18 Rotation speed: 300 rpm
# tracks per surface: 80 Head motion: 3 msec to move 1 track
 | Seek time | Latency | Transfer time | Total
Best |  |  |  | 
Worst |  |  |  | 
Average |  |  |  | 

## Slide 23: Magnetic Disks
Notes: Hard disk drive… with 5mb of storage
In september 1956, ibm launched the 305 RAMAC, the first ‘super’ computer with a hard disk drive. The hard disk drive weighed over a ton and stored 5MB of data.

## Slide 24: Optical Disks
CD
A compact disk that uses a laser to read information stored optically on a plastic-coated disk; data is evenly distributed around spiral track
CD-ROM read-only memory
CD-DA digital audio
CD-WORM write once, read many
RW or RAM both read from and written to
DVD
Digital Versatile Disk, used for storing audio and video
Blu-ray
Higher capacity DVD allowing higher resolution video, etc.

## Slide 25: Flash Drives
Flash Memory
Nonvolatile
Can be erased and rewritten
Supports USB mass storage standard
Notes: 25

## Slide 26: Memory (Primary/Secondary)
Cache memory
Principle of locality
When information is needed, it:
  looks in cache
  accesses desired info from RAM
  copies data into cache

## Slide 27: Memory (Primary/Secondary)
Summary:
Primary Memory | Secondary Memory

## Slide 28: Arithmetic/Logic Unit
Performs basic arithmetic operations such as addition and subtraction
Performs logical operations such as AND, OR, and NOT
Most modern ALUs have a small amount of special storage units called registers that can be accessed faster than main memory

## Slide 29: Control Unit
Control unit
The organizing force in the computer
Instruction register (IR)
Contains the instruction that is being executed
Program counter (PC)
Contains the address of the next instruction to be
executed
Central Processing Unit (CPU)
ALU and the control unit called the Central Processing Unit, or CPU

## Slide 30: Flow of Information
Bus
In general: A communication system that transfers data between components inside a computer or between computers; the medium (wires, optical fiber, etc.) and the protocols (rules for sharing the medium nicely)
“The” bus: Connects the CPU, main memory, I/O devices, and possibly other components (e.g. hard disk drive)

## Slide 31: What is an N-bit Processor?
It could mean any of these:
N-bit general registers
N-bit ALU
N-bit addresses
N-bit data bus

## Slide 32: The Fetch-Execute Cycle
Fetch the next instruction
Decode the instruction
Get data if needed
Execute the instruction
Why is it called a cycle?

## Slide 33: The Fetch-Execute Cycle

## Slide 34: Embedded Systems
34
Embedded systems
Computers that are dedicated to perform
a narrow range of functions as part of a
larger system
Empty your pockets or backpacks.
How many embedded systems do you have?
Notes: 34

## Slide 35: Instructions, cont’d
Typical format of machine language instruction
Ex: ADD X,Y
op code
address1
address2
…

## Slide 36: Instruction Set
Numeric code | Meaning | 
0000 | load x | x  R
0001 | store x | R  x
0010 | clear x | 0  x
0011 | add x | R + x  R
0100 | increment x | x + 1  x
0101 | subtract x | R - x  R
0110 | decrement x | x – 1  x
0111 | compare x | if x > R then 100  CCR else if x < R then 001  CCR else if x = R then 010  CCR
1000 | jump x | goto x
1001 | jumpgt x | goto x if CCR=100
1010 | jumpeq x | goto x if CCR=010
1011 | jumplt x | goto x if CCR=001
1100 | jumpneq x | goto x if CCR<>010
1101 | in x | store input in x
1110 | out x | output x
1111 | halt |